## Slide 1
INTELLIGENT PARKING ASSISTANCE SYSTEM USING ARM CORTEX-M3
Smart Distance Detection and Automated Parking Barrier Control
Team Member | Roll Number
Mangalagiri Shirisha | 2510080017
Keerthi Varna | 2510080023
Shravika | 2510080036
Praneeth Reddy | 2510080051
Arun Reddy | 2510080062
Team Name: [Team Name]
Department & University: [Department, University]
Faculty Mentor: [Faculty Mentor]
Academic Year: [Academic Year]
ARM
Cortex-M3
HC-SR04
Obstacle
d = ?
Parking guidance LEDs

## Slide 2: Abstract and Project Overview
This project presents an embedded parking assistant built on an ARM Cortex-M3 microcontroller. An HC-SR04 ultrasonic sensor measures the distance to an obstacle using timer-based echo pulse measurement, while an IR sensor detects vehicle presence. Red, yellow and green LEDs give visual guidance, a PWM-driven DC motor and a relay simulate the parking barrier and gate, a push button provides interrupt-based user control, and UART reports distance and status to a serial monitor.
1
Obstacle distance measurement
2
Vehicle presence detection
3
Visual parking guidance
4
Automated barrier simulation
5
Serial monitoring and user control
System overview
Sensors
Ultrasonic · IR · Button
ARM Cortex-M3
GPIO · Timer · PWM · NVIC · UART
Outputs
LEDs · Motor · Relay · UART

## Slide 3: Problem Statement and Motivation
The Challenge
Confined spaces make it hard for drivers to judge the distance to walls or vehicles. Manual control of parking access is also slow and inconsistent.
The Motivation
Low-cost sensors with a microcontroller can give timely distance warnings and show how automatic gate control works.
The Approach
Measure distance with ultrasound, detect vehicles with IR, warn with LEDs, and actuate a barrier with PWM and a relay.
Aspect | This Prototype | Real Safety-Certified System
Sensing | Single HC-SR04 and IR sensor | Redundant, weather-robust sensors
Barrier | Small DC motor and relay demo | Industrial actuator with safety interlocks
Standards | Educational demonstration | Certified, fail-safe, tested to standards
Note: the prototype is for learning and demonstration only and must not be relied on for real vehicle safety.

## Slide 4: Objectives
1
Configure ultrasonic sensing using GPIO trigger control
2
Measure echo pulse width using a hardware timer
3
Calculate obstacle distance
4
Detect vehicle presence using an IR sensor
5
Control red, yellow and green LEDs by distance
6
Generate timer-based PWM for a DC motor barrier
7
Control a relay to represent the parking gate
8
Configure a push button as an external interrupt
9
Assign suitable NVIC interrupt priorities
10
Transmit distance and status through UART
11
Explain the Cortex-M3 memory map and peripheral registers

## Slide 5: System Architecture / Block Diagram
HC-SR04
Ultrasonic Sensor
IR Vehicle
Sensor
Push Button
ARM Cortex-M3 MCU
GPIO
Timer / Input Capture
PWM Timer
NVIC + EXTI
UART
TRIG
ECHO
IR OUT (digital)
EXTI line
Red / Yellow / Green LEDs
GPIO
Motor Driver + DC Motor
(barrier)
PWM
Relay Module
(parking gate)
GPIO
USB-UART Adapter
Serial Monitor
TX
Inputs

## Slide 6: Hardware Components and Their Functions
Component | Function | Interfacing Consideration
ARM Cortex-M3 board | Main controller running all logic | Any Cortex-M3 board; 3.3 V logic typical
HC-SR04 ultrasonic | Measures distance via echo pulse | Needs 5 V; divide ECHO to 3.3 V
IR obstacle sensor | Detects vehicle presence (digital) | Check output level; tune sensitivity pot
3 LEDs + resistors | Red/yellow/green parking guidance | About 330 Ω each to limit current
DC motor + driver | Simulates parking barrier arm | Driver required; flyback protection
Relay module | Represents parking gate switching | Driver/opto input; separate load supply
Push button | External interrupt user control | Pull-up/down resistor; debounce
Power supply | Powers MCU, sensors and motor | Separate motor supply; common ground
USB-to-UART adapter | Serial link to PC terminal | Cross TX/RX; match 3.3 V levels

## Slide 7: Complete Circuit Diagram and Wiring
Cortex-M3 Board
(example GPIO labels)
HC-SR04
VCC 5V · GND
TRIG ← PA0 (out)
ECHO → PA1 (TIMx_CH) via divider
IR Sensor
VCC · GND
OUT → PA2 (GPIO in)
Push Button
to GND, pull-up
PB0 (EXTI0), active low
Power: 5 V / 3.3 V logic supply,
separate motor supply,
common GND
R / Y / G LEDs + 330 Ω each
PB5
PB6
PB7
Motor
Driver
DC
Motor
PA6 PWM (TIMx_CHy)
Relay Module
(parking gate)
PB8 GPIO out
USB-UART Adapter → PC
PA9 UART TX → RX
Safety: pins are examples only; final pins depend on the selected MCU board. Never drive a motor or relay coil from a GPIO. HC-SR04 ECHO is 5 V, so use a divider or level shifter. Use flyback protection and a common ground.

## Slide 8: Working Process / Program Flow
Initialise clock, GPIO, timer, NVIC, UART
1
Send 10 µs pulse on TRIG
2
Capture ECHO rising and falling edges
3
Compute distance from pulse width
4
Read IR sensor for vehicle presence
5
Set R/Y/G LED by distance zone
6
Drive barrier: PWM motor and relay
7
Send status over UART, then repeat
8
Button interrupt (parallel): pressing the button triggers an ISR that sets a flag for manual override or gate lock; the main loop reads the flag and acts.

## Slide 9: Ultrasonic Distance Measurement
Timing diagram
TRIG
ECHO
10 µs
Echo pulse width t
Timer capture:
rising edge = start
falling edge = stop
8 ultrasonic bursts sent
Formula
d = (t × v) / 2, v ≈ 343 m/s
d (cm) ≈ t (µs) / 58
Example
t = 1160 µs → d ≈ 20 cm
Divide by 2: sound travels out and back.
Timer set-up
Prescale to a 1 µs tick, use input capture on both edges, and add a timeout if no echo returns.

## Slide 10: Distance Zones and LED Indication
Example thresholds (tunable in firmware)
SAFE
> 30 cm
CAUTION
15 – 30 cm
DANGER
< 15 cm
Far from obstacle
Close to obstacle
Zone | Active LED | Driver Meaning | UART Status
Safe | Green | Continue slowly | SAFE
Caution | Yellow | Prepare to stop | CAUTION
Danger | Red | Stop immediately | DANGER
Only one LED is on at a time; each LED uses its own resistor and GPIO pin.

## Slide 11: Barrier Control: PWM Motor and Relay Gate
PWM duty cycle controls motor speed
25%
50%
75%
Motor driver sits between MCU and motor; MCU only supplies the PWM signal.
Event | Motor (PWM) | Relay (Gate)
Vehicle detected by IR | Duty up: barrier opens | Energised
Vehicle clear + delay | Reverse: barrier closes | De-energised
Danger zone (red) | Hold / stop motor | Keep closed
Button: manual lock | Stop; ignore IR | Held closed
Relay modules are often active-low; confirm in the module datasheet.

## Slide 12: External Interrupt and NVIC Priorities
Button press
EXTI line
(falling edge)
NVIC
(priority check)
ISR sets flag
Main loop acts
Interrupt | Example Priority | Reason
Timer input capture (ECHO) | 0 (highest) | Timing-critical edge capture
Push button EXTI | 1 | Quick user response
UART | 2 (lowest) | Not time-critical
Key Points
• On Cortex-M3, a lower number means higher priority.
• Higher-priority interrupts can pre-empt lower ones.
• Keep ISRs short; debounce the button; clear flags.
• Priorities are set with NVIC registers (e.g. NVIC_SetPriority).

## Slide 13: UART Serial Communication
Cortex-M3
UART TX
USB-UART
Adapter
PC Serial
Monitor
Example settings: 9600 baud, 8 data bits, no parity, 1 stop bit (8N1)
DIST=45 cm | IR=0 | LED=GREEN | GATE=CLOSED
DIST=22 cm | IR=0 | LED=YELLOW | GATE=CLOSED
DIST=12 cm | IR=1 | LED=RED | GATE=OPEN
Sample format (illustrative, not measured data)
Wiring Notes
Cross TX to RX and RX to TX. Share a common ground. Match the 3.3 V logic level of the board.

## Slide 14: Cortex-M3 Memory Map and Peripheral Registers
0xE010_0000 – 0xFFFF_FFFF
Vendor-specific
0xE000_0000 – 0xE00F_FFFF
Private peripheral bus: NVIC, SysTick
0xA000_0000 – 0xDFFF_FFFF
External device
0x6000_0000 – 0x9FFF_FFFF
External RAM
0x4000_0000 – 0x5FFF_FFFF
Peripherals: GPIO, TIMx, UART, EXTI
0x2000_0000 – 0x3FFF_FFFF
SRAM: stack and data
0x0000_0000 – 0x1FFF_FFFF
Code: Flash, vector table
Register Access
Peripheral registers are memory-mapped: base address + offset, accessed through volatile pointers.
Bit-Banding
SRAM alias at 0x2200_0000 and peripheral alias at 0x4200_0000 give atomic single-bit access.
Exact peripheral base addresses depend on the MCU vendor.

## Slide 15: Conclusion, Limitations and Future Scope
Conclusion
The system combines ultrasonic ranging, IR detection, PWM, relay control, interrupts and UART on a Cortex-M3, covering core embedded concepts in one project.
Limitations
Single sensor, limited range and angle, example thresholds, and a demonstration barrier that is not safety certified.
Future Scope
Multiple sensors, filtering, LCD or buzzer alerts, RTOS scheduling, wireless monitoring and automatic number plate recognition.
Thank You
Shirisha · Keerthi Varna · Shravika · Praneeth Reddy · Arun Reddy